## Slide 1: Geiger Tube Theory, Dead Time
22.S902 – DIY Geiger Counters
Prof. Michael Short

## Slide 2: Questions to Start
2
Where is the best place to extract our count rate signal?
What is the highest count rate that we can detect?
Courtesy of Mark Chilenski. Used with permission.

## Slide 3: Motivation
3
Understand how ionization chambers, and specifically Geiger tubes, function
Learn the mechanism of “dead time” in detectors, and how it limits them
Characterize detectors as paralyzable or not
Predict how dead time will affect counting output and statistics

## Slide 4: Geiger-Müller Tubes
4
An SBM-20U tube, showing the wire anode
Our SBM-20 Geiger tubes
Courtesy of Images SI, Inc. Used with permission.

## Slide 5: Our SBM-20 Geiger-Müller Tubes
5
Wall thickness: 50μm steel
Wall Density: 8 g/cm3
Assume 1 atm equal gas mixture
For more information, see: http://www.gstube.com/data/2398/
Tube diagram © source unknown. All rights reserved. This content is
excluded from our Creative Commons license. For more information,
see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 6: Ionization Chambers
6
+
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
Public domain image.
Geiger tube photo courtesy of Jeff Keyzer on Flickr.
Circuit diagram © Wiley-VCH, from J. Turner, Atoms, Radiation, and
Radiation Protection (2007). All rights reserved. This content is
excluded from our Creative Commons license. For more information,
see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 7: The Ionization Plateau (Low-V)
7
+
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
Public domain image.
Graph © Wiley-VCH. All rights reserved. This content is excluded from our Creative Commons license. For more information, see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 8: The Ionization Plateau (Med-V)
8
+
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
Public domain image.
Graph © Wiley-VCH. All rights reserved. This content is excluded from our Creative Commons license. For more information, see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 9: The Ionization Plateau (High-V)
9
+
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
Public domain image.
Graph © Wiley-VCH. All rights reserved. This content is excluded from our Creative Commons license. For more information, see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 10: The Ionization Plateau (HIGH-V)
10
+
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
Public domain image.
Graph © Wiley-VCH. All rights reserved. This content is excluded from our Creative Commons license. For more information, see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 11: Now for the Math…
Let’s say a gamma flux of enters a chamber of area A. Each makes N ion pairs, each with a charge of e and energy W, and then stops in the chamber:
The charge produced per particle is , and the number of particles entering per second is . That makes the current I:
11
+
Radiation “Intensity”

## Slide 12: Now for the Math…
Let’s say a gamma flux of enters a chamber of area A. Each makes N ion pairs, each with a charge of e and energy W, and then stops in the chamber:
Now use the radiation
intensity:
12
+
Radiation “Intensity”

## Slide 13: Now for the Math…
Let’s say a gamma flux of enters a chamber of area A. Each makes N ion pairs, each with a charge of e and energy W, and then stops in the chamber:
The absorption rate of energy in the chamber is
These can be used to measure gamma ray energy, proportional to the measured current!
13
+
Radiation “Intensity”

## Slide 14: Our Use: A Simple Counter
14
+
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
Public domain image.
Geiger tube photo courtesy of Jeff Keyzer on Flickr.
Circuit diagram © Wiley-VCH, from J. Turner, Atoms, Radiation, and Radiation Protection (2007). All rights reserved. This content
is excluded from our Creative Commons license. For more information, see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 15: Our Use: A Simple Counter
15
We use circuitry to detect the rising edge of the pulse from the Geiger tube
Set some threshold to call the edge risen
Send this (now digital) signal to our LEDs and the speaker to make light and nose!
Public domain image.
Geiger tube photo courtesy of Jeff Keyzer on Flickr.
Circuit diagram © Wiley-VCH, from J. Turner, Atoms, Radiation, and
Radiation Protection (2007). All rights reserved. This content is
excluded from our Creative Commons license. For more information,
see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 16: Let’s Re-Examine Our Circuit
© Wiley-VCH. All rights reserved. This content is excluded from our Creative Commons license. For more information, see http://ocw.mit.edu/help/faq-fair-use/.
16
That’s our rising edge trigger!
Courtesy of Mark Chilenski. Used with permission.

## Slide 17: Look Closer: Rising Edge Trigger
17
Transistor is both a switch and an inverter
555 timer is triggered to charge its capacitor (charge bucket) until full
This signal is sent to speakers and LEDs
Courtesy of Mark Chilenski. Used with permission.

## Slide 18: Our Measured Waveforms
18
Actual SBM-20 Geiger tube waveform
Pulse stretcher (sound and light) waveform

## Slide 19: Limiting Cases: High Signal
19
What happens if LOTS of counts come in at once?
No problem!
Missed count!
This is known as “dead time,” a period when the detector is unresponsive
GM Tube
Pulse Stretcher

## Slide 20: Paralyzable vs. Non-Paralyzable
Image by MIT OpenCourseWare.
Which applies to our cases?
GM Tube
Pulse Stretcher

## Slide 21: Paralyzable vs. Non-Paralyzable
GM Tube
Pulse Stretcher
+
Increase count rate
Geiger tube photo courtesy of Jeff Keyzer on Flickr. Circuit diagram © Wiley-VCH. All rights reserved. This content is excluded from our Creative Commons license. For more information see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 22: Paralyzable vs. Non-Paralyzable
GM Tube
+
Very rapid radiation events keep the ion current high
This maintains the circuit voltage
above the rising edge trigger threshold
The GM tube is therefore paralyzable,
but its dead time is very low (<1μs)
Geiger tube photo courtesy of Jeff Keyzer on Flickr. Circuit diagram © Wiley-VCH. All rights reserved. This content is excluded from our Creative Commons license. For more information see http://ocw.mit.edu/help/faq-fair-use/.

## Slide 23: Paralyzable vs. Non-Paralyzable
Pulse Stretcher
Very rapid radiation events
don’t re-trigger capacitor discharge
No additional time is spent at logic high voltage
The pulse stretcher is therefore non-paralyzable,
but its dead time is very high (~1.5ms)

## Slide 24: Thinking Ahead for the Lab
24
How will you characterize GM dead time?
How will you characterize pulse stretcher dead time?
Where on your circuit will you connect the computer to measure counts?
What other sources of dead time exist in the system? Hint: There are some!

## Slide 25
25

## Slide 26
MITOpenCourseWare
http://ocw.mit.edu
22.S902 Do-It-Yourself (DIY) Geiger Counters
January IAP 2015
For information about citing these materials or our Terms of Use, visit: http://ocw.mit.edu/terms.